## Slide 1: Adaptive Charging Network
LACI, December 2018
Steven Low
Notes: Caltech ACN
Dec 9, 2016: GlobalSIP, Washington DC (invited Meng Wang)
March 30, 2017 NSF: Barbara Kenny, Prakash Balan AIR PM, Arlington, VA
February 12, 2018: Real-time learning & decision making in dynamic systems, NSF Workshop (Le Xie, TAMU)
August 4, 2018: NSF Workshop on real-time learning & decision making for grid resilience (ANURAG K SRIVASTAVA)
Sept 19, 2018: Caltech Facilities (John Onderdonk)
Dec 12, 2018: LACI (Ken Pickar)

## Slide 2
2012
2017
research
commercialization
Incubation to launch
Energy mgt research
EV Charging
Joint DER opt +
Energy Services
Notes: Our vision for PF also has two stages: In PF Stage 1, we will build a product to provide large-scale EV charging at minimum capital and operating costs. In PF Stage 2 when we have a large number of EVs under management, we will also provide energy services to ISOs and utilities on top of our EV management platform. Both revenue streams are critical to make the venture work.
CalSEED I was one of the earliest grants we received that helped get PF Stage 1 started. We were also lucky enough to have received NSF SBIR I and Wells Fargo/NREL’s IN2 grant around the same time. We are actively building the technologies and business for large-scale EV charging.
CalSEED II will allow us to explore some of our Stage 2 ideas, while continue to build our Stage 1 business.
In the following, we will first explain what we have achieved during CalSEED Phase 1, the motivating problem, our solution, the product we have built, its performance and market traction to date, as well as projections and financials.
We will then propose an R&D plan with the CalSEED Phase 2 grant that builds on our CalSEED 1 results, how it fits into our business plan, and how it will benefit CA ratepayers and help advance CEC’s energy goals.

## Slide 3
Watershed Moment
Bell: telephone
1876
Tesla: multi-phase AC
1888
both started as natural monopolies
both provided a single commodity
both grew rapidly through two WWs
1980-90s
Deregulation
started
IoT
1969: DARPAnet
convergence
to Internet
Deregulation
started
1980-90s

## Slide 4
Watershed Moment
What will drive power
network transformation?
Power system will undergo a similar architectural transformation that communication network went through
  Industry will be restructured
  Infrastructure will be reshaped
  Control paradigms will be upended
  Markets will be revolutionized
(April 2017)

## Slide 5
Electricity Generation and Transportation
Consumes 2/3 of All Energy and Emits 1/2 of All Greenhouse Gases (2014)
Source: USEPA

## Slide 6
Today’s Grid
Few large generators
  ~10K bulk generators, actively controlled
Many dump loads
  131M customers, ~billion passive loads
Control paradigm: Schedule supply to match demand
  Centralized, human-in-the-loop, worst-case, deterministic

## Slide 7
Future Grid
Wind and solar farms are not dispatchable
  Many small distributed generations
Network of distributed energy resources (DERs)
  EVs, smart buildings/appliances, wind turbines, storage
Control paradigm: Adapt demand to volatile supply
  Distributed, real-time feedback, risk limiting, robust

## Slide 8
Scale: Billions of DERs are coming as IoT emerges...
Source: International Energy Agency - World Energy Outlook
Historic data vs IEA WEO predictions (GW of annual added capacity)

## Slide 9
Caltech Research
Risk
Active DERs introduce rapid random
fluctuations in supply, demand, power quality, increasing risk of blackouts
Foundational theory, practical algorithms, concrete applications
Integrate engineering and economics
Active collaboration with industry
Opportunity
Active DERs enable real-time dynamic network-wide feedback control, improving robustness, security, efficiency
Distributed control of networked DERs

## Slide 10
Sample Projects
Projects on DERs
  Control & optimization
  Markets and market power
  NREL testbeds
  EV charging deployment

## Slide 11
2012
2017
research
commercialization
Incubation to launch
Energy mgt research
funding >$10M
EV Charging
Joint DER opt +
Energy Services
Notes: Our vision for PF also has two stages: In PF Stage 1, we will build a product to provide large-scale EV charging at minimum capital and operating costs. In PF Stage 2 when we have a large number of EVs under management, we will also provide energy services to ISOs and utilities on top of our EV management platform. Both revenue streams are critical to make the venture work.
CalSEED I was one of the earliest grants we received that helped get PF Stage 1 started. We were also lucky enough to have received NSF SBIR I and Wells Fargo/NREL’s IN2 grant around the same time. We are actively building the technologies and business for large-scale EV charging.
CalSEED II will allow us to explore some of our Stage 2 ideas, while continue to build our Stage 1 business.
In the following, we will first explain what we have achieved during CalSEED Phase 1, the motivating problem, our solution, the product we have built, its performance and market traction to date, as well as projections and financials.
We will then propose an R&D plan with the CalSEED Phase 2 grant that builds on our CalSEED 1 results, how it fits into our business plan, and how it will benefit CA ratepayers and help advance CEC’s energy goals.

## Slide 12: Agenda
Caltech Adaptive charging network (ACN)
  Physical infrastructure
  Charging statistics
  Research platform
Model and algorithms
  Linear program
  Smoothed least laxity first

## Slide 13
ACN: physical infrastructure

## Slide 15: Caltech Adaptive Charging Network

## Slide 16: Caltech Adaptive Charging Network

## Slide 17: Caltech Adaptive Charging Network
Operational since 2016
Experimental platform in continuous development
Delivered ~550MWh (by 9/2018)
Equivalent to 1.7M miles, 570 tons of avoided CO2e

## Slide 18: Caltech Adaptive Charging Network
 | Emerging product | Online LP | Theoretical max
Caltech | 28% | 53% | 54%
industry
standard
our algorithm
Theorem (Guo, Erliksson, Low, 2016)
Online LP attains offline optimal
Early theory work:
Gan, Topcu, Low, Optimal decentralized protocol
for EV charging, IEEE Trans. on Power Systems, 2013

## Slide 19
Deployment
Sept 2018

## Slide 20
ACN: statistics

## Slide 21
Caltech ACN
Caltech ACN snapshot Sept 17, 2018
today’s
energy delivered
charging station utilization
power utilization
energy delivered & impact to date
peak power

## Slide 22
Caltech ACN
2016: 67 MWh
2017: 186 MWh
2018: 191 MWh

## Slide 23
Caltech ACN
may
june
july
august
septemer
20
40
60
80
100
daily #charging sessions (April 15 – Sept 18, 2018)

## Slide 24
Caltech ACN
Caltech ACN
April 15 – Sept 18, 2018
hourly # charging sessions
weighted averages

## Slide 25
Caltech ACN
hourly aggregate charging power
weighted averages
Caltech ACN
April 15 – Sept 18, 2018

## Slide 26
Caltech ACN
Caltech ACN
April 15 – Sept 18, 2018

## Slide 27
Caltech ACN
Caltech ACN
April 15 – Sept 18, 2018

## Slide 28
Caltech ACN
Caltech ACN
June 1-29, 2018
Total# sessions: 1,780
arrival & departure hours
duration
energy delivered

## Slide 29
Caltech ACN
cumulate charging current
Jan 2018

## Slide 30
Caltech ACN
Spatial utilization snapshot (June 1 – August 31, 2018)
 | total | per day | per space | remark
#parking spaces | 53 |  |  | 
#days (June 1 – Aug 31, 2018) | 92 |  |  | inc. weekends
#charging sessions | 6,103 | 66 | 115 | >1 session /space/day
occupancy (space-day) | 3,374 | 37 | 64 | 69% occupancy
energy delivered (kWh) | 54,562 | 593 | 1,029 | 11 kWh /space/day
#hours occupied | 28,407 | 309 | 536 | 5.8 hours /space/day

## Slide 31
CAN: ongoing research

## Slide 32: Undergrad research
ACN used for 16 undergrad projects (2016 – 2018)
  22 undergrads: 20 Caltech, 2 Lund (Sweden), 4 female
  2016: 1 class project, 1 Directed Study, 4 SURF projects
  2017: 1 class project, 2 Directed Studies
  2018: 5 class projects, 1 Directed Studies, 1 SURF project
Notes: Critical gap in algorithm research. The mathematical or simulation models used in algo- rithm research for smart grid tend to be drastically simpler (and often unrealistic) compared to a real system for which an algorithm is designed. By abstracting away many complicating details, mathematical analysis often allows us to uncover hidden structures of the problem, leading to new qualitative insights and new algorithmic designs. There is however a sizable gap between theo- retical results and a robust and high performance implementation of an algorithm. If one aspires to apply some of one’s theory results to design algorithms that can make an impact in practice, bridging this gap will be critical. It will require, beyond mathematical analysis:
1. Detailed simulations driven by realistic models and data. 2. The ability to test an algorithm implementation in the field.
Often, the bottleneck in crossing this gap is the lack of realistic models and data for simulations and opportunity for field test. We propose to build a novel infrastructure to help overcome this bottleneck and enable new algorithm research in the smart grid space, especially electric vehicles research.

## Slide 33: Undergrad research
Karl Erliksson 2016 SURF (Lund)
  ACN visualization
Notes: Critical gap in algorithm research. The mathematical or simulation models used in algo- rithm research for smart grid tend to be drastically simpler (and often unrealistic) compared to a real system for which an algorithm is designed. By abstracting away many complicating details, mathematical analysis often allows us to uncover hidden structures of the problem, leading to new qualitative insights and new algorithmic designs. There is however a sizable gap between theo- retical results and a robust and high performance implementation of an algorithm. If one aspires to apply some of one’s theory results to design algorithms that can make an impact in practice, bridging this gap will be critical. It will require, beyond mathematical analysis:
1. Detailed simulations driven by realistic models and data. 2. The ability to test an algorithm implementation in the field.
Often, the bottleneck in crossing this gap is the lack of realistic models and data for simulations and opportunity for field test. We propose to build a novel infrastructure to help overcome this bottleneck and enable new algorithm research in the smart grid space, especially electric vehicles research.

## Slide 34: Live testbed
Motivation
  Math or simulation models in algorithms research tend to be unrealistic
  Bridging gap between theory and practice requires realistic models & data for simulations and opportunity for field test
Notes: Critical gap in algorithm research. The mathematical or simulation models used in algo- rithm research for smart grid tend to be drastically simpler (and often unrealistic) compared to a real system for which an algorithm is designed. By abstracting away many complicating details, mathematical analysis often allows us to uncover hidden structures of the problem, leading to new qualitative insights and new algorithmic designs. There is however a sizable gap between theo- retical results and a robust and high performance implementation of an algorithm. If one aspires to apply some of one’s theory results to design algorithms that can make an impact in practice, bridging this gap will be critical. It will require, beyond mathematical analysis:
1. Detailed simulations driven by realistic models and data. 2. The ability to test an algorithm implementation in the field.
Often, the bottleneck in crossing this gap is the lack of realistic models and data for simulations and opportunity for field test. We propose to build a novel infrastructure to help overcome this bottleneck and enable new algorithm research in the smart grid space, especially electric vehicles research.

## Slide 35
Live testbed
Notes: The goal of the proposed project is to develop a suite of software and hardware that will make Caltech ACN not just a production EV charging facility after mid 2018, but also a live testbed for researchers at, and outside, Caltech. It will enable research on data science and online algorithms for smart grid, based on real driver behavior and real charging data.
Our basic idea is to treat the production ACN as a physical layer and create an intermediate layer, called the ACN Research Portal, that will have a well-designed interface to the PowerFlex management system in the cloud. The Research Portal both provides interfaces and clean anonymized data to, and protects the physical layer from, the research layer above.
System components. The ACN Research Portal consists of three main components.
1. A data acquisition system that will automatically collect, extract, clean, anonymize, and visualize high-resolution charging data in real time.
2. A data-driven simulator that can drive simulations by replaying real consumer behavior and mimicking the behavior of batteries and chargers using models derived from real data. This simulator will also automatically evaluate the safety, security, and performance of a charging or pricing algorithm for suit- ability before deploying the algorithm on ACN.
3. An experimental platform that will allow safe, secure and reliable real-world testing of new online algorithms on ACN along side the production algorithm. It captures all the complications of a physical system that are abstracted away in a simulation model, and demands a higher degree of

## Slide 36
CA Duck Curve
Oct 22, 2016
Shift service
Shimmy service
Source: 2025 CA DR Potential Study (LBNL 2017)
EV potential for grid service
  Behind-the-meter DR potential will only increase
    CA: 50% renewables by 2030, 100% by 2045
    CA: 1.5M ZEV by 2025, 5M by 2030
  Potential value of EV for DR service @1.5M EVs : $50B / yr (2025)
Notes: Unique strengths
  Team has been working together for 15 years at Caltech and FastSoft
  Leading experts in energy systems, networking, cloud-computing
  ... covering EV charging, advance algorithms, software dev, IT, protocols
  Experience in startup, invention, building & managing talented team

## Slide 37
CA Duck Curve
Oct 22, 2016
3M EV workplace charging
@10kWh/EV
Shift service
Shimmy service
Source: 2025 CA DR Potential Study (LBNL 2017)
 | Annual DR value
Shift service | $190 / EV
Shimmy service | $150 / EV
@1.5M EV | $50B
EV potential for grid service
  Behind-the-meter DR potential will only increase
    CA: 50% renewables by 2030, 100% by 2045
    CA: 1.5M ZEV by 2025, 5M by 2030
  Potential value of EV for DR service @1.5M EVs : $50B / yr (2025)
Assumptions: DR value from 2025 CA DR Potential
Study (LBNL 2017); each EV drives 12K miles/year,
needs 11kWh/day, workplace charging; 10% provide DR
Notes: Unique strengths
  Team has been working together for 15 years at Caltech and FastSoft
  Leading experts in energy systems, networking, cloud-computing
  ... covering EV charging, advance algorithms, software dev, IT, protocols
  Experience in startup, invention, building & managing talented team

## Slide 38
. . .
distribution
grid
transmission
grid
PF cloud
ACN input
utility input
ISO input
utilities
ISO markets
driver
input
ACN
PF cloud
input
driver
input
ACN
PF cloud
input

## Slide 39
Duck Curve & DCM
NREL: demand charge mitigation (Nov 2018)
Filling Duck Curve valley and maintaining total net load to grid between 30 kW – 40 kW
On weekdays: building load is much higher and much more volatile
building – PV (weekday)
building – PV + EV
building – PV (weekend)
Weekend Duck Curve: building baseload (10kW) – PV
Notes: This is an NREL experiment where DCM is running on a building that has PV (previous experiment did not have PV). The experiment started today, which is why I didn't have a plot like this before...
See Ted’s email Oct 15, 2018
The blue line is an NREL building site load + PV. The duck curve is apparent here.
The orange line is the NREL building site load + PV + EVs with DCM. There is a high bump in the orange between 7:30AM and 9:30AM because I had to make some settings changes. These changes were finished at 9:30AM and you can see the orange line was pretty stable for the rest of the day. Tomorrow's plot will look pretty flat.

## Slide 40: Online tracking
PV
charging rate
(EVSE)
Real-time tracking of PV generation at JPL (10/2016)

## Slide 41: Agenda
Caltech Adaptive charging network (ACN)
  Physical infrastructure
  Charging statistics
  Research platform
Model and algorithms
  Linear program
  Smoothed least laxity first

## Slide 42
Model and algorithms:
LP

## Slide 43: Charging model
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)

## Slide 44: Charging model

## Slide 45: Offline optimal charging
Offline optimal problem is a linear program
charge only after ai before di
not exceeding peak rate

## Slide 46: Offline optimal charging
Offline optimal problem is a linear program
meet energy demand
not exceed limit;
can generalize to
linear constraints

## Slide 47: Online LP
Offline LP is not implementable
  It needs future EV information
Implement Online LP
  Solve LP with current EVs, assuming no future arrival
  Update remaining energy demand after each online LP iteration
  Model-predictive control

## Slide 48: Performance: online LP
Suppose cost coefficients are uniformly monotone
Theorem
If online LP is feasible, then it attains offline optimal
Guo, Erliksson, L. PES GM 2017

## Slide 49: Performance: online LP
Theorem
competitive ratio can be arbitrarily bad
Guo, Erliksson, L. PES GM 2017

## Slide 50: Performance: online LP
feasibility of online LP
~ feasibility of offline LP
(averaged over all locations
and all days for each dataset)
normalized difference
normalized difference

## Slide 51
Data cleaning
Remaining #EVs (charging sessions)
Mountain View: 44,587
Sunnyvale: 6,466
CA Garage: 1,309
Total: 52,362 sessions, in 2016 (over a few months)
104 locations
>4,000 charging days
Notes: The transformer capacity is 7.2 kW (25 kW shared between 4 houses). Each car can charge at a peak rate of 7.2 kW. Therefore all three cars charging at their peak rate will exceed the transformer limit.
The demo will run over 11 minutes with the following scenario:
Three cars will be plugged in at different times with different energy demands and departure times:
  Car 1: arrives at time 0, departs at time 11 mins, needs 0.71 kWh.
  Car 2: arrives at time 2 mins, departs at 5 mins, needs 0.36 kWh.
  Car 3: arrives at time 3 mins, departs at 8 mins, needs 0.25 kWh.
The scenario is designed to illustrate the importance of smart charging (and other system functions; see below):
  Dumb charging where each car charges at its peak will exceed transformer limit.
  Static sharing policy will not satisfy EV energy demands.
  Only dynamic adaptation based on real-time information can work, as shown in the diagram below.

## Slide 52: Performance
peak demand reduction
Caltech data (Feb – May, 2016)
savings = infrastructure, demand charge
data: g2016mtv2000
data: CAgarage2016

## Slide 53
Conclusions
savings increase in initial laxity
significant savings even at low laxity
Adaptive charging network
ACN min peak power
reducing capital &
operating costs
Daily peak power | Unmanaged charging (kW) | PF (kW) | Power savings
Caltech | 85.3 | 33.8 | 60%
Mountain View | 46.2 | 28.4 | 39%
Sunnyvale | 94.0 | 56.2 | 40%
Karl Erliksson 2016 SURF
Notes: The transformer capacity is 7.2 kW (25 kW shared between 4 houses). Each car can charge at a peak rate of 7.2 kW. Therefore all three cars charging at their peak rate will exceed the transformer limit.
The demo will run over 11 minutes with the following scenario:
Three cars will be plugged in at different times with different energy demands and departure times:
  Car 1: arrives at time 0, departs at time 11 mins, needs 0.71 kWh.
  Car 2: arrives at time 2 mins, departs at 5 mins, needs 0.36 kWh.
  Car 3: arrives at time 3 mins, departs at 8 mins, needs 0.25 kWh.
The scenario is designed to illustrate the importance of smart charging (and other system functions; see below):
  Dumb charging where each car charges at its peak will exceed transformer limit.
  Static sharing policy will not satisfy EV energy demands.
  Only dynamic adaptation based on real-time information can work, as shown in the diagram below.

## Slide 54
Model and algorithms:
sLLF

## Slide 55: Smoothed Least laxity first (sLLF)
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)
no look-ahead

## Slide 56: Smoothed Least laxity first (sLLF)
energy
demand
(miles / kWh)
arrival /
departure
time
peak
charging
rate (kW)
remaining
time
minimum
required

## Slide 57: Smoothed Least laxity first (sLLF)
Algorithm: max min laxity at next time
Nakahira, et al, e-Energy 2017

## Slide 58: Smoothed Least laxity first (sLLF)
 water-filling algorithm
Theorem
sLLF rates solves
Nakahira, et al, e-Energy 2017

## Slide 59: Smoothed Least laxity first (sLLF)
Theorem
sLLF rates are
Proportionally fair
Maxmin fair
Nakahira, et al, e-Energy 2017

## Slide 60: Smoothed Least laxity first (sLLF)